## Slide 1: VGA Transpose and Edge Detection
Team 7 - Distance Learning Students
Bryce Williams - GTID: 903097901
Zachary Boe - GTID: 903124261
Gregory Walls - GTID: 903289298
Benjamin Sullins - GTID: 903232988

## Slide 2
Completed Design Will Provide:
  User Selectable Video Output Options
  On/Off Transpose
  On/Off Edge Detection
  VGA Formatted Video Output
Project Overview
User DIP Switch Inputs
Internal VHDL Firmware
VGA Connector/Cable
DIP Switch Inputs
VGA Monitor
Basys 3 Board

## Slide 3: Chip Architecture/Memory Design
Fake Camera:
MMCM – Clock and Reset Provider
State Machine – Controls Frame Generation
Counter Controller – Controls Location Within Frame
Output Controller – Strobe/Data Generation
BRAM – Preloaded *.coe Test Image
Mux – User Selectable Output Selection
Notes: Top Level Generics Establish Output Frame Size, Frame Rate, Bit Depth
Transpose Circuit:
M

## Slide 4: Chip Architecture/Memory Design
Edge Detection:
Streamed 8-bit Data Input
Two 3x3 Filters (Separable Matrix Configuration/Row-Column); Vertical and Horizontal Filter
Muxed Output Select: Original, Vertical, Horizontal, or Sum of Gradients Image (8-bit)
Dynamic Latency Compensation for Frame and Line Valid Signals
Two N-bit Block RAM Line Buffers (Feed both Vertical and Horizontal Images)
VGA Formatter:
MMCM – Clock and Reset Provider
BRAM – Serves as a clock domain crossing element
  New incoming images overwrite the BRAM address space at incoming clock rate
  Address space is read out according to VGA specs at clock rate corresponding to output resolution
Syncs – Counters are kept at VGA clock rate to determine correct timing and duration for sync signals
BRAM
Clk
VGAClk
Video
Video
HSync
VSync

## Slide 5: Architectural Alternatives
Fake Camera:
Slice Logic |  |  |  |  | 
Site Type |  | Used | Fixed | Available | Util%
Slice LUTs |  | 74 | 0 | 20800 | 0.36
 | LUT as Logic | 74 | 0 | 20800 | 0.36
 | LUT as Memory | 0 | 0 | 9600 | 0
Slice Registers |  | 77 | 0 | 41600 | 0.19
 | Register as Flip Flop | 77 | 0 | 41600 | 0.19
 | Register as Latch | 0 | 0 | 41600 | 0
F7 Muxes |  | 8 | 0 | 16300 | 0.05
F8 Muxes |  | 0 | 0 | 8150 | 0
Design Timing Summary |  | 
WNS(ns) | WHS(ns) | WPWS(ns)
13.938 | 0.06 | 3
Power | 
Total On-Chip Power (W) | 0.199
Dynamic (W) | 0.127
Device Static (W) | 0.072
Effective TJA (C/W) | 5
Max Ambient (C) | 84
Junction Temperature (C) | 26
Confidence Level | Low
Setting File | ---
Simulation Activity File | ---
Design Nets Matched | NA
Memory |  |  |  | 
Site Type | Used | Fixed | Available | Util%
Block RAM Tile | 5 | 0 | 50 | 10
RAMB36/FIFO* | 5 | 0 | 50 | 10
RAMB36E1 only | 5 |  |  | 
RAMB18 | 0 | 0 | 100 | 0
Design Verified Operational At 100 MHz (System Clock)
Design Outputs Verified:
  Horizontal Test Bars
  Vertical Test Bars
  Preloaded Test Image
Design Throughput Verified:
  Valid Pixels : 160
  Valid Lines : 120
  Invalid Pixels: 16
  Bit Depth : 8 (Monochrome)
  Pixel Rate: 50 MHz

## Slide 6: Architectural Alternatives
Transpose Circuit:
Slice Logic |  |  |  |  | 
Site Type |  | Used | Fixed | Available | Util%
Slice LUTs |  |  |  | 20800 | 
 | LUT as Logic |  |  | 20800 | 
 | LUT as Memory |  |  | 9600 | 
Slice Registers |  |  |  | 41600 | 
 | Register as Flip Flop |  |  | 41600 | 
 | Register as Latch |  |  | 41600 | 
F7 Muxes |  |  |  | 16300 | 
F8 Muxes |  |  |  | 8150 | 
Design Timing Summary |  | 
WNS(ns) | WHS(ns) | WPWS(ns)
Power | 
Total On-Chip Power (W) | 
Dynamic (W) | 
Device Static (W) | 
Effective TJA (C/W) | 
Max Ambient (C) | 
Junction Temperature (C) | 
Confidence Level | 
Setting File | 
Simulation Activity File | 
Design Nets Matched | 
Memory |  |  |  | 
Site Type | Used | Fixed | Available | Util%
Block RAM Tile |  |  | 50 | 
RAMB36/FIFO* |  |  | 50 | 
RAMB36E1 only |  |  |  | 
RAMB18 |  |  | 100 | 
Design

## Slide 7: Architectural Alternatives
Edge Detection:
Current design uses 2x separable multiplier banks per filter with shared line buffers; reduces filter operation complexity and line buffers only required to be as wide as data samples
Alternatives include:
  Single MCM filter block
    Implements Full/Inseparable Matrix Operations; Increased filter operation complexity and BRAM Line Buffers require larger data widths
  N-MCM filter block
    Implements Full/Inseparable Matrix Operations; Increased filter operation complexity
Slice Logic |  |  |  |  | 
Site Type |  | Used | Fixed | Available | Util%
Slice LUTs |  | 231 |  | 20800 | 
 | LUT as Logic | 198 |  | 20800 | 
 | LUT as Memory | 33 |  | 9600 | 
Slice Registers |  | 608 |  | 41600 | 
 | Register as Flip Flop | 608 |  | 41600 | 
 | Register as Latch | 0 |  | 41600 | 
F7 Muxes |  | 0 |  | 16300 | 
F8 Muxes |  | 0 |  | 8150 | 
Power | 
Total On-Chip Power (W) | 6.964
Dynamic (W) | 6.861
Device Static (W) | 0.103
Effective TJA (C/W) | 5.0
Max Ambient (C) | 50.2
Junction Temperature (C) | 59.8
Confidence Level | Low
Setting File | 
Simulation Activity File | 
Design Nets Matched | NA
Memory |  |  |  | 
Site Type | Used | Fixed | Available | Util%
Block RAM Tile | 1 |  | 50 | 
RAMB36/FIFO* | 0 |  | 50 | 
RAMB36E1 only | 2 |  |  | 
RAMB18 | 2 |  | 100 | 

## Slide 8: Architectural Alternatives
VGA Converter:
Slice Logic |  |  |  |  | 
Site Type |  | Used | Fixed | Available | Util%
Slice LUTs |  | 168 | 0 | 20800 | 0.81
 | LUT as Logic | 168 | 0 | 20800 | 0.81
 | LUT as Memory | 0 | 0 | 9600 | 
Slice Registers |  | 135 | 0 | 41600 | 0.32
 | Register as Flip Flop | 135 | 0 | 41600 | 0.32
 | Register as Latch |  | 0 | 41600 | 0
F7 Muxes |  | 8 | 0 | 16300 | 0.05
F8 Muxes |  | 0 | 0 | 8150 | 0
Design Timing Summary |  | 
WNS(ns) | WHS(ns) | WPWS(ns)
13.938 | 0.06 | 3
Power | 
Total On-Chip Power (W) | 0.199
Dynamic (W) | 0.127
Device Static (W) | 0.072
Effective TJA (C/W) | 5
Max Ambient (C) | 84
Junction Temperature (C) | 26
Confidence Level | Low
Setting File | ---
Simulation Activity File | ---
Design Nets Matched | NA
Memory |  |  |  | 
Site Type | Used | Fixed | Available | Util%
Block RAM Tile | 9 | 0 | 50 | 38
RAMB36/FIFO* | 9 | 0 | 50 | 38
RAMB36E1 only | 9 |  |  | 
RAMB18 | 0 | 0 | 100 | 0
VGA Timings Are Set In Stone – No Alternatives Except Different Resolutions
Dual Frame Buffer
  Eliminate Frame Flicker When Switching Frames
  Suited More For Continuously Changing Frames (Video)
  Would Require Dropping Information On The BRAM Input Side

## Slide 9: Final Design Review Plans
Fake Camera:
Transpose Circuit:
M
Generate Additional Preloaded Test Images for Verification (Right)
Actual Output Seen Below (Grayscale Yoshi.png)
Bonus: ColorMapping Circuit Completed (Pink Yoshi.png)
No Additional Plans Needed

## Slide 10: Final Design Review Plans
Edge Detection:
VGA Converter:
Generate Additional Test Patters To Verify Correct VGA Timings
Additional Debug To Eliminate Sporadic Issues
Code Cleanup
Resize And Integrate Line Buffers According To Final Decision On Image Width
All Objectives Completed; Refine Product As Needed
Actual Post-processed Simulation Results Seen To The Right

## Slide 11
Milestones | Oct. 30th | Nov. 2nd | Nov. 12th | Nov. 19th | Nov. 25th | Nov. 30th
Requirements / Concept Design |  |  |  |  |  | 
Sub-Module Design Capture |  |  |  |  |  | 
Sub-Module Design Test and Peer Review |  |  |  |  |  | 
Sub-Module Integration |  |  |  |  |  | 
Project Abstract |  |  |  |  |  | 
Project PDR |  |  |  |  |  | 
Project CDR |  |  |  |  |  | 
Final Presentation |  |  |  |  |  | 
Schedule/Milestones
Description:
Work Assignments:
Project Abstract – Nov 2nd, 2017
Project PDR – Nov 12th, 2017
Project CDR – Nov 19th, 2017
Final Presentation – Nov, 30th 2017
Bryce Williams : Edge Detection
Zachary Boe : VGA Formatter
Gregory Walls : Transpose Circuit
Benjamin Sullins : Fake Camera Sim.
Legend: Complete Incomplete (Milestones – All Team Members)

## Slide 12: Status/Risks Met
Fake Camera Simulator
POC: Benjamin Sullins
100% Complete
Horizontal Test Pattern Complete
Vertical Test Pattern Complete
Preloaded Test Image Complete
All Tasks Verified In ISIM
Transpose Circuit
Edge Detection
VGA Formatter
POC: Zachary Boe
95% Complete
Horizontal Sync Complete
Vertical Sync Complete
BRAM Addressing Complete
Functional Verification In Process
MATLAB Algorithm Reference and Image Data Generator for VHDL Sim (Complete)
MATLAB Post-Processing Script (Complete)
Fully Implemented VHDL Sobel Filter with Output Select (Complete)
VHDL Simulation/Verification of Design (Complete)

## Slide 13: Additional Slides (Remove When Submitting)

## Slide 14: Chip Architecture/Memory Design
Fake Camera:
Transpose:
Basys 3 Development hardware
Top-Level MMCM
State Machine
Counter Controller
Clk
Output Controller
BRAM
Video Output
Test Image
*.coe
DIP Switch Inputs
Basys 3 Board