## Slide 1: VGA Transpose and Edge Detection
Team 7 - Distance Learning Students
Bryce Williams - GTID: 903097901
Zachary Boe -
Gregory Walls - GTID: 903289298
Benjamin Sullins - GTID: 903232988

## Slide 2
Project Overview
Basys 3 Development hardware
Description:
Develop A Processing System For Generating Synthetic Images, Transposing, Detecting Edges, and Displaying Video To A VGA Monitor.
Hardware Implemented On A Basys 3 Development Board
Firmware Written In VHDL Within Vivado 2017.2
Fake Camera Simulator
Transpose Circuit
Edge Detection
VGA Formatter

## Slide 3: Subsystem Description
Fake Camera Simulator
Generate Synthetic Video
  Horizontal Ramp Test Pattern
  Vertical Ramp Test Pattern
  Pre-Loaded Cropped Image
Replicates Real-Life Camera Output
  CameraLink Pixel Clock Rates - 50 MHz
  Image Size – 160x120
  Frame Rate – 50 Hz
  Monochrome
Transpose Circuit
Selectable Video Output
  Non-Transposed
  Transposed
Retains Input Video Format
Retains Input Video Frame Rate
Retains Input Video Pixel Clock Rate
Edge Detection
Selectable Video Output
  Unfiltered
  Edge Detection Filtered
Sobel Edge Detection
  3x3 Kernel
  Vertical and Horizontal Edge Detection
Retains Input Video Format
Retains Input Video Frame Rate
Retains Input Video Pixel Clock Rate
VGA Formatter
VGA Video Format Converter
  Pixel Clock Rate - 21.175 MHz
  Image Size - 640x480
  Frame Rate – 60 Hz
Clock Domain Transferring
Image Up-scaling
Grayscale

## Slide 4
Optimizations
Fake Camera Simulator
Consolidate Individual Frame FVAL/LVAL Control Signal Generations To Single Module
Reduce Resource Utilization For Horizontal/Vertical Ramp Test Pattern Data Generation
Transpose Circuit
Reduce Resource Utilization by shrinking the BRAM IP as much as possible
Edge Detection
VGA Formatter
Reduce Resource Utilization for Vertical and Horizontal Filters (Shared Line-Buffers)
Reduce Resource Utilization for Line-Buffers (IP BMG)
TODO

## Slide 5
Milestones | Oct. 30th | Nov. 2nd | Nov. 12th | Nov. 19th | Nov. 25th | Nov. 30th
Requirements / Concept Design |  |  |  |  |  | 
Sub-Module Design Capture |  |  |  |  |  | 
Sub-Module Design Test and Peer Review |  |  |  |  |  | 
Sub-Module Integration |  |  |  |  |  | 
Project Abstract |  |  |  |  |  | 
Project PDR |  |  |  |  |  | 
Project CDR |  |  |  |  |  | 
Final Presentation |  |  |  |  |  | 
Timeline
Description:
Work Assignments:
Project Abstract – Nov 2nd, 2017
Project PDR – Nov 12th, 2017
Project CDR – Nov 19th, 2017
Final Presentation – Nov, 30th 2017
Bryce Williams : Edge Detection
Zachary Boe : VGA Formatter
Gregory Walls : Transpose Circuit
Benjamin Sullins : Fake Camera Sim.
Legend: Complete Incomplete (Milestones – All Team Members)

## Slide 6
Risk Mitigation
Fake Camera Simulator
Horizontal/Vertical Ramp Test Pattern Generation Simulated With Matlab
Pre-Loaded Cropped Image Simulated With Matlab
All Data Output Options Simulated With ISIM
Transpose Circuit
ISIM Code Verification Using Synthetic Images
Use VGA Monitor to Visually Verify Correct Functionality
Edge Detection
VGA Formatter
Algorithm Implementation in MATLAB
MATLAB Generated Image Data for VHDL Simulation
MATLAB Post-Processing of VHDL Simulation Output Data
TODO

## Slide 7
Fake Camera Simulator
CameraLink Standard
  http://www.imagelabs.com/wp-content/uploads/2010/10/CameraLink5.pdf
  Defines Commercial Video Transmission Standard Used By Large Varieties Of Cameras
  Defines Allowable Pixel Clock Range 25-85 MHz
  “Camera Link is a communication interface for vision applications. The interface extends the base technology of Channel Link to provide a specification more useful for vision applications.”
Frame Control Signals
  https://www.imperx.com/wp-content/uploads/Member/Whitepapers/camera_link.ppt
  Standard Framing Strobes Used For Video Output
  Used Widespread Across Commercial Cameras
  CameraLink Protocol Supported
    “de Facto standard for high speed/high resolution imaging”
Test Pattern Options
  https://www.xilinx.com/support/documentation/ip_documentation/v_tpg/v7_0/pg103-v-tpg.pdf
  Describes Example Test Patterns
  Generic Overview Of Test Pattern Generation
  Generic Overview Of Frame Control Signals
  “Test patterns can be used to evaluate and debug color, quality, edge, and motion performance, debug and assess video system color, quality, edge, and motion performance of a system, or stress the video processing to ensure proper functionality.
Prior Work

## Slide 8
Prior Work – Cont.
Transpose Circuit
Transpose
Edge Detection
Meyer-Baese, Uwe (2014). Digital Signal Processing with Field Programmable Gate Arrays, Fourth Edition. Berlin Heidelberg: Springer-Verlag
  Image Processing Overview
  2D HDL Filter Design and Architecture

## Slide 9
Prior Work – Cont.
VGA Formatter
VGA

## Slide 10
Expected Results
Fake Camera Simulator
Valid Pixels Per Line : 160
Invalid Pixels Per Line : 16
Valid Lines : 120
Pixel Clock : 50 MHz
Frame Rate : 50 Hz
Video Selection Changes Based On User DIP Switch Input
Transpose Circuit
Switch Logic Low:
  Original Image is Output
Switch Logic High:
  Transpose Image is Output
Edge Detection
VGA Formatter
TODO
Latency: ~2*Line Width
Sample Rate: 1 cycle
Pixel Clock: 50 MHz
Frame Rate: 50 Hz
Output Select: Vertical/Horizontal/Sum

## Slide 11
Completed Design Will Provide:
  User Selectable Video Output Options
  On/Off Transpose
  On/Off Edge Detection
  VGA Formatted Video Output
Expected Results
User DIP Switch Inputs
Internal VHDL Firmware
VGA Connector/Cable
DIP Switch Inputs
VGA Monitor
Basys 3 Board